## Slide 1
Human activity Recognition with Wi-Fi Using Machine Learning for Building Automation and Energy Saving
Tanmay Mane
Supervisor – Prof. Dr.-Ing. H. C. Jürgen Becker
Advisor - Prof. Dr.-Ing. Adolfo Bauchspiess, M. Sc. Iris Walter

## Slide 2: Introduction
Increasing energy consumption
Meeting the world's energy needs sustainably is a current challenge
50% - HVAC. Residential buildings share - 26%, non-residential buildings had 10%.
Next 30 years – Energy demands increases by 50% - 60%
Energy Consumption of global buildings

## Slide 3: Research Objective
HAR through sensors
ML and Optimization
Enenrgy saving for building automation
Smart Building Energy Management (SBEM) technology.
Reduces carbon emissions, Energy costs, and enhancing user comfort.
Solution - Device-free Human activity recognition (HAR) with Wi-Fi signals using ML.
The overview of HAR with Wi-Fi using ML

## Slide 4: Theoretical Background
ESP32 NodeMCU -
802.11b/g/n
4 MB SPI flash
Low-cost Microcontroller
ESPNOW Protocol -
2.4 GHz wireless connection
Peer to peer connection. Pairing required
Use call-back function.
Works with MAC address header
Max working range ~ 400 meters
ESPNOW
OFDM -
Channel State Information -
Multiple orthogonal sub-carrier
Reduced ICI and ISI
CSI for each Carrier
High data rate
Spatial multiplexing
Spatial Diversity
CSI amplitude
CSI phase
How signal travels from Tx to Rx
Amplitude attenuation and phase shift for ENV, Human activity
Tx
Rx
MIMO -

## Slide 5: Theoretical Background
Convolution Neural Network (CNN) -
Reinforcement Learning (RL)-
Q - Learning -
Deep Q –Learning Network (DQN) -
Process data that has grid pattern
Next possible estimated best action
Exploration and Exploitation
learning method
output
sit
walk
stand
Agent>action>Env>reward
Model-free approach
Q-value - measure an action at a particular state
Neural Network instead of Q - table
Epsilon-Greedy exploration strategy
Bellman Equation -
Bellman Equation -

## Slide 6: State of the Art
2D CNN as Recognition algorithm
Reinforcement Learning - LSTM
5 activities performed by 7 persons.
97% on unseen Person, 2D CNN – 99%
Location- and Person-Independent Activity Recognition with WiFi, Deep Neural Networks, and Reinforcement
Learning - Y. Ma.
WiAgent: Link Selection for CSI-Based Activity Recognition in Densely Deployed Wi-Fi Environments - 2021 IEEE
Case 1: Use a Wi-Fi link selected by WiAgent.
Case 2: Use two orthogonal Wi-Fi links.
Case 3: Use all Wi-Fi links.
Architecture - CNN, LSTM

## Slide 7: The Framework of HAR
Data Acquisition
ESP32 NodeMCU
ESPNOW protocol
CSI Information
HAR with WIFI
Antenna Setup
Tx – 2
Rx - 5
Data Preprocessing
Cleaning CSI Data
-delete & Insert
CSI amplitude
CSI denoising
Phase sanitization
PCA analysis
Data labeling
Segmentation
Feature Representation
CNN Block
Data augmentation
Convolution
Max pooling
Fully connected Network
Model training
Image classification
Accuracy/Loss on Transfer Learning
Reinforcement Learning
Create ENV
DQN network
Reward, action
Image classification
Accuracy/Loss on transfer Learning
Application
Activity Recognition
Transfer Learning

## Slide 8: Data Acquisition
Training ENV_1
Framework of CSI transmission
Test ENV_2
M1
M2
S8
S3
S4
S5
S6
S7
S7
S6
S5
S4
S3
M2
M1
M1 starts the process with broadcast.
CSI enable.
M2 sends the broadcast.
M1 collects CSI from all sensors.
Use TDMA
Same acquisition time.
Sensor configuration setup
Tx – 2 ESP32
Rx – 6 ESP32
Features are similar
10 links, 1 Antenna
M1:M2 S3:S8
54 subcarrier.
10*54 = 540 useful samples.
Define Cycle = 75 // 750 ms

## Slide 9: Data Acquisition
Sit
Stand
Empty
Walk
Sit
Stand
Walk
Empty
Configuration Setup
Tx – 2 ESP32
Rx – 5 ESP32
4 Activities – 4 classes
Sit – 30 sec
Stand – 30 sec
Walk – 30 sec
Empty – 30 sec
Antenna Direction Vertical
Antenna Direction Horizontal
Data collection of 4 different person for Training ENV_1 and Test ENV_2.
Total 2 min Activity HAR
Person 1 in Training ENV_1
Person 1 in Test ENV_2
1 cycle of CSI data

## Slide 10: Data Preprocessing
Clean CSI data -
Insert and delete misbehaving lines in CSI data acquisition
Remove unwanted Noise
Phase sanitization of the data.
CSI image with amplitude and phase -
PCA component – 24
25 cycles per 10 sec
PCA
Cycle per 10 sec
Subcarrier length
Im and Re part gets separated and mapped Am and Pha
CSI Image with activities
25 cycles/10 sec
75 cycles/30 sec

## Slide 11: Data Preprocessing
Consecutive CSI from sensor 3 with varying subcarrier
CSI image with Am and Pha combine
PCA transformation
Apply
12 image frames per 2 min experiment
For training – 4 person 2 min activity – sit, stand, walk, empty
12 * 4 = 48 Images for Vertical Antenna direction
12 * 4 = 48 Images for Horizontal Antenna direction
CSI PCA images >> feed to Neural network
All 54 carriers combine with activity for S3 sensor
Sit
Sit
Sit
Stand
Stand
Stand
Walk

## Slide 12: Feature Representation
Convolutional NN approach
CSI HAR – Tx – 2 and Rx – 5
Sit, Stand, Walk, Empty
96 data Images
batch_size = 4
criterion = nn.CrossEntropyLoss()
optimizer = optim.Adam(model.parameters(), lr=0.0001)
num_epochs = 50
self.label_map = {"empty": 0, "sit": 1, "stand": 2, "walk": 3}
Best acc: 42.553%
65 train images
31 test images
Use data augmentation approach -
Random crop size
Horizontal flip
Vertical flip
Rotation range
Adaptation and Improvements
Use 2D Conv layer
Increase no. of epoch
Add drop layer – 0.3
Resizing of image (24*24)
Best acc: 83.333%

## Slide 13: Feature Representation
Best acc: 93.055%
Layer | Name | Size | Parameters | Activation
1 | Conv 2D | Kernel 3 x 3(16) | Stride = 2 | ReLU
2 | Max pooling | Kernel 2 x 2 | Stride = 2 | none
3 | Conv 2D | Kernel 3 x 3(32) | Stride = 2 | ReLU
4 | Dropout | none | Rate = 0.3 | none
5 | Max pooling | Kernel 2 x 2 | Stride = 2 | none
6 | FC | 4 | none | Softmax
7 | FC | 4 | none | Softmax
Increase depth
Use two dense layer
Softmax classifier

## Slide 14: Reinforcement Learning
Reinforcement learning using Q-learning
Q-learning parameters -
CSI HAR – Tx – 2 and Rx – 5
Sit, Stand, Walk, Empty
96 data Images
Reward –
Every correct action = 0.3
Every wrong action = -0.3
Best acc: 13.553%
Adaptation and Improvements
Combine approach -
2D CNN model with Q – network
Replace Q – table with NN
Build DQN model
Build the custom Environment using OpenAI gym
classActivityRecognitionEnv(gym.Env):
env = ImageClassificationEnvironment(n_classes=4) agent = QLearningAgent(n_classes=4)
Batch size – 32
Discount factor – 0.9
Learning rate – 0.001
Target update Freq – 20
No of episodes - 1000
Parameters | Initial Values | Adaptations
Batch Size | 32 | 30
Discount Factor | 0.9 | 0.8
Learning Rate | 0.001 | 0.00025
Target update Freq. | 20 | 10
Reward for correct action | +0.3 | +0.1
Reward for Negative action | -0.3 | -0.1
Optimizer |  | Adam

## Slide 15: Reinforcement Learning
Initialization
Data preprocessing
Training Loop
Episode Init.
Action selection
Env Interaction
Store experience
Sample batch
Q-value update
Exploration
Check for Termination
Convergence Check
Model Deployment for Decision
Validation of RL using DQN
Best Test accuracy – 75%
Validation Loss – 1.09
Train Loss – 1.13
Training -

## Slide 16: Transfer Learning Results
Cross Environment Validation using only CNN
Training ENV_1
Test ENV_2
Person 1
Person 1
Best Test accuracy – 88%
Validation Loss – 1.00
Train Loss – 0.98
Unknown location known person –
Best Test accuracy – 79%
Validation Loss – 1.09
Train Loss – 1.05
Cross Environment Validation using DQN
Best Test accuracy – 73%
Validation Loss – 1.16
Train Loss – 1.15
Best Test accuracy – 69%
Validation Loss – 1.17
Train Loss – 1.18
Unknown location unknown person –
Unknown location known person –
Unknown location unknown person –

## Slide 17: Results
Results and Observed points -
4 different activity, 4 person, Antenna direction
Horizontal antenna setup made a very negligible difference.
Performance of the CNN is better.

## Slide 18: Conclusion and Future Scope
Transfer Learning possible
Device free Wi-Fi sensing.
HAR without using camera and RFID is big advantage
IoT integrated building automation – Thermal comfort, energy saving.
RL algorithm required large amount of data
Future Scope -
Incorporating additional sensors for better data.
Energy saving in HVAC, securities, vehicles.
Real time HAR for building automation.

## Slide 19
Thank to…..
Prof. Dr.-Ing. Dr. H. C. Jürgen Becker
Prof. Dr.-Ing. Adolfo Bauchspiess
M. Sc. Iris Walter